ECE 301

HW #9

wlg

Due:  November 15,  ‘07			            	     Name_______________________

Use engineering paper.  Work only on one side of the paper.  Use this sheet as your cover sheet, placed on top of your work and stapled in the top left-hand corner.  Number the problems at the top of the page, in the center of the sheet.  Do neat work.  Underline your answers.  Show how you got your equations.  Be sure to show how you got your answers.  Each problem counts 15 points.

This set of homework will help you get ready for Test #3.

  - Sinusoidal Definition:

Ans:     Vm = 3 V;  T = 0.3 sec;  f = 2 Hz;   ( = 4(; ( = -45o;   v(t) = 3cos(4(t – 45o)  V;

V = 3(-45o V

  - Nodal Analysis:

Ans:  V1 = 9.4(29.6o V,  V2 = 4.99(111.5o V

  - Mesh Analysis:

Ans:     I1 =   0.94(-150.4o A,       I2 =   1.05(-177o A,     I3 =  0.997(-158.6o  A

  - Nodal Analysis:

Ans:   V1 = 20.33(-23.5o V

  - Mesh Analysis:

Ans:   I1 =  1.64(80.5o  A,     I2 =   2.98(74.2o A

  - Nodal Analysis:

Ans:  V1 = 0 V

  - Mesh Analysis:

Ans:   I1 =  2(0o  A,      I2 =   0

  - Thevenin:

Work part (a) only and find only the Thevenin equivalent circuit.

Ans:  VTH = 200(0o V,      ZTH = 111.8(26.6o (